## Slide 1: Default implementation of tfm_ns_interface_dispatch()

## Slide 2: Current state of the code
PSA functions (e.g. psa_connect, psa_call, …)
tfm_ns_interface_dispatch() which should provide:
Multithread safety based on the NS OS (or bare metal implementation)
Other application needs
- Provided by TFM
- Expected to be provided by user

## Slide 3: Example implementation
int32_t tfm_ns_interface_dispatch(veneer_fn fn,
uint32_t arg0, uint32_t arg1,
uint32_t arg2, uint32_t arg3)
{
int32_t result;
/* TFM request protected by NS lock */
while (os_wrapper_mutex_acquire(ns_lock_handle, OS_WRAPPER_WAIT_FOREVER)
!= OS_WRAPPER_SUCCESS);
result = fn(arg0, arg1, arg2, arg3);
while (os_wrapper_mutex_release(ns_lock_handle) != OS_WRAPPER_SUCCESS);
return result;
}
tfm_ns_interface_dispatch()
tfm_ns_interface_dispatch()
uint32_t tfm_ns_interface_init(void)
{
void *handle;
handle = os_wrapper_mutex_create();
if (!handle) {
return OS_WRAPPER_ERROR;
}
ns_lock_handle = handle;
return OS_WRAPPER_SUCCESS;
}

## Slide 4: Problem statement
Currently TF-M requires users to provide implementation of tfm_ns_interface_dispatch().
The problem here is that each user have to implement this function, which means that users need to read documentation, write, test and maintain the code. This is not ideal user experience.
Default (example) implementation of this function should be suitable for most of the use cases. So the proposal is to provide implementation of this function as part of NS interface install folder and have os_wrapper_*() function be provided by NS OS.
This solution is same as one done for multicore mailbox, where NS OS is expected to provide implmentation of tfm_ns_mailbox_os_*() functions.
This way most of the users will have less code to write and maintain. Users that previously used custom implementations of this functions can still use them instead of the default one.
Firs step to this improvement was done by creating a patch to FreeRToS to provide NS OS wrapper functions (see implementation here).
See next slide for more details.

## Slide 5: Structure change proposal
PSA functions (e.g. psa_connect, psa_call, …)
tfm_ns_interface_dispatch()
- Provided by TFM
- Default implementation is provided by TFM, but can be replaced with user custom implementation
tfm_ns_interface_init()
os_wrapper_mutex_acquire()
os_wrapper_mutex_release()
os_wrapper_mutex_create()
os_wrapper_mutex_ delete()
- Provided by NS OS

## Slide 6: Proposed supported use cases (NS OSs)
Following use cases (NS OSs) are proposed to be supported by default:
Free RToS
CMSIS RToS v2
Bare metal environment
Zephyr (If the community is interested)
This list covers lots of the use cases and is suitable for lots of users.